## Slide 1
Computer Organization & Assembly Language
Lecture 05
by Omar Bin Samin

## Slide 2: Today’s Discussion
What is NASM?
DosBox, NASM and AFD installation
Assembly Language Example

## Slide 3: NASM
NASM stands for “Netwide Assembler”
It is considered as one of the most popular assemblers for Linux
It is an assembler for the Intel x86 architecture
It can be used to write 16-bit, 32-bit (IA-32) and 64-bit (AMD-64) programs

## Slide 4: NASM Setup
Download DOSBox, NASM and AFD from the following link:
https://github.com/omar-samin/Computer-Organization-Assembly-Language
Extract the downloaded file, following 2 files and 1 folder will be extracted:
  DOSBox0.74.exe
  DOSBox 0.74.3.3.dmg
  NASM+AFD

## Slide 5
First install DOSBox. It is a virtual machine
Copy “NASM+AFD” folder from the extracted directory and paste it in a local drive and rename the folder to “COAL”
NASM is an assembler while AFD is a debugger
To program and work in this environment, create a new source file with “.asm” extension in the same folder and open it in desired application (.e.g. Notepad)

## Slide 6
Copy the following program in the created file:
  [org 0x0100]
  mov ax,2
  mov bx,2
  add ax, bx
  mov ax,0x4c00 ; exit
  int 0x21 ; OS should perform the above operation
Save the file and open DOSBox
Mount the required directory using the following command:
  mount c c:/COAL

## Slide 7
Now this path becomes the drive of virtual machine
To assemble, follow the given steps:
  C:
  nasm L3.asm –o L3.com
To open Advance Free Debugger, use the following command:
  afd L3.com

## Slide 8
To see addresses in memory using Window M1, use the following command:
  m1 0100
To quit Advance Free Debugger, use the following command:
  quit
To get listing file, use the following command:
  nasm L3.asm –l L3.lst –o L3.com

## Slide 9: Listing File
1 [org 0x0100]
2 00000000 B80200 mov ax,2
3 00000003 BB0200 mov bx,2
4 00000006 01D8 add ax, bx
5 00000008 B8004C mov ax,0x4c00
6 0000000B CD21 int 0x21

## Slide 10
Video lecture can be accessed at
https://www.youtube.com/watch?v=0-M1uXZZotw