## Slide 1
Computer Organization & Assembly Language
Lecture 10
by Omar Bin Samin

## Slide 2: Today’s Discussion
Loop Instructions
  Unconditional
  Conditional

## Slide 3: Loop Instructions
Loop instructions are used to execute the given instructions for required number of times
There are two types of loop instructions:
  Unconditional Loop Instructions
  Conditional Loop Instructions

## Slide 4: Unconditional Loop Instructions
These instructions are used to loop a group of instructions until the condition satisfies, i.e. CX = 0
Syntax:
  loop tag

## Slide 5
Consider the following piece of code:
  [org 0x0100]
  mov bx, 5
  add ax, bx
  add bx, 2
  add ax, bx
  add bx, 2
  add ax, bx
  add bx, 2
  mov ax,0x4c00
  int 0x21
Same instructions are repeated 3 times

## Slide 6
Same task as discussed in the previous slide can also be implemented using unconditional loops. Consider the following piece of code:
  [org 0x0100]
  mov bx, 5
  mov cx, 3
  Tag:
  add ax, bx
  add bx,2
  loop Tag
  mov ax,0x4c00
  int 0x21

## Slide 7: Task 01
Show values of AX, BX and CX for all executable instructions.
  [org 0x0100]
  xor ax,ax
  xor bx,bx
  xor cx,cx
  mov al,1
  mov bl,7
  mov cl,3
  Tag1:
  add al,bl
  loop Tag1
  mov ax,0x4c00 ; exit
  int 0x21

## Slide 8: Task 02
Generate the table of 2 using mul operation and unconditional loop instruction such that the program exits when destination register value is equal to 0A.

## Slide 9: Conditional Loop Instructions
In these types of instructions, the processor must check for the particular condition. If it is true + CX !=0, only then the loop executes
The arithmetic and logic operations set flags
The conditional loop statements tests the flag and jump if the relevant flag is set along with CX !=0
Conditional loop instructions are as follows:
  LOOPE / LOOPZ
  LOOPNE / LOOPNZ

## Slide 10: LOOPE / LOOPZ
LOOPE stands for ‘Loop if Equal’
LOOPZ stands for ‘Loop if Zero’
  Decrements CX
  If CX !=0 and ZF = 1, then jumps to label/tag
  Else, execute next instruction

## Slide 11: LOOPNE / LOOPNZ
LOOPNE stands for ‘Loop if Not Equal’
LOOPNZ stands for ‘Loop if Not Zero’
  Decrements CX
  If CX !=0 and ZF = 0, then jumps to label/tag
  Else, execute next instruction

## Slide 12: Example 01
Show values of AX, BX, CX and ZF for all executable instructions.
  [org 0x0100]
  mov al,1
  mov bl,2
  mov cl,5
  Tag1:
  add al,bl
  cmp al,3
  loopz Tag1
  Mov ax,0xFFFF
  mov ax,0x4c00
  int 0x21

## Slide 13: Solution
AX |  | BX |  | CX |  | ZF
AH | AL | BH | BL | CH | CL | 
00 | 01 | 00 | 00 | 00 | 00 | 0
00 | 01 | 00 | 02 | 00 | 00 | 0
00 | 01 | 00 | 02 | 00 | 05 | 0
00 | 03 | 00 | 02 | 00 | 05 | 0
00 | 03 | 00 | 02 | 00 | 05 | 1
00 | 03 | 00 | 02 | 00 | 04 | 1
00 | 05 | 00 | 02 | 00 | 04 | 0
00 | 05 | 00 | 02 | 00 | 04 | 0
00 | 05 | 00 | 02 | 00 | 03 | 0
FF | FF | 00 | 02 | 00 | 03 | 0

## Slide 14: Task 03
Generate the following sequence using conditional loop instruction “loopne”:
  1
  3
  9
  1B
  51

## Slide 15
Video lecture can be accessed at
https://www.youtube.com/watch?v=lcE-ddIHLPM