## Slide 1
Computer Organization & Assembly Language
Lecture 04
by Omar Bin Samin

## Slide 2: Today’s Discussion
8086 Registers

## Slide 3: 8086 Registers
Registers are high-speed storage locations directly inside the CPU, designed to be accessed at much higher speed than conventional memory
These registers are grouped into 3 categories:
  Segment registers
  General registers
  Control registers

## Slide 4: Segment Registers

## Slide 5: Segment Registers
Segments are specific areas defined in a program for containing data, code and stack
Code Segment
Data Segment
Stack Segment
Extra/ Extended Segment

## Slide 6
Code Segment (CS)
  It contains all the instructions to be executed
  A 16-bit Code Segment Register or CS Register stores the starting address of the code segment
Data Segment (DS)
  It contains all the variables (data)
  A 16-bit Data Segment Register or DS Register stores the starting address of the data segment

## Slide 7
Stack Segment (SS)
  It contains data and return addresses of subroutines
  A 16-bit Stack Segment Register or SS Register stores the starting address of the stack segment
Extra/ Extended Segment (ES)
  It is used to store variables (data), incase the data segment is not sufficient to store all variables
  A 16-bit Extra/ Extended Segment Register or ES Register stores the starting address of the extra segment

## Slide 8: General Registers

## Slide 9: General Registers
The general registers are further divided into the following three groups:
  Data Registers
  Pointer Registers
  Index Registers

## Slide 10: 1. Data Registers
Four 16-bit data registers are used for arithmetic, logical and other operations
AX - Accumulator Register
BX - Base Register
CX - Count Register
DX - Data Register

## Slide 11
These 16-bit registers can be divided into two halves. i.e., 8-bit each
16-bit | 8-bit (High) | 8-bit (Low)
AX | AH | AL
BX | BH | BL
CX | CH | CL
DX | DH | DL

## Slide 12: General Knowledge
64-bit | 32-bit | 16-bit | 8-bit (High) | 8-bit (Low)
RAX | EAX | AX | AH | AL
RBX | EBX | BX | BH | BL
RCX | ECX | CX | CH | CL
RDX | EDX | DX | DH | DL

## Slide 13
AX (Accumulator Register)
AX is a 16-bit register in which intermediate arithmetic and logic results are stored
BX (Base Register)
BX is a 16-bit register which can hold the address of a variable or can also be used as an AX helper for arithmetic and logic operations
CX (Counter Register)
CX is a 16-bit register which acts as a counter for loop instructions or can also be used as an AX helper for arithmetic and logic operations

## Slide 14
DX (Data Register)
DX is a 16-bit register which can be used to store data for I/O operations and it also can:
  Holds the high 16 bits of the product in multiply
  Holds the remainder of the divide operations
It can also be used as an AX helper for arithmetic and logic operations

## Slide 15: 2. Pointer Registers
Two 16-bit pointer registers used in 16-bit architecture are:
SP - Stack Pointer
BP - Base Pointer

## Slide 16
SP (Stack Pointer)
  The 16-bit SP register is the stack pointer, used to manage push and pop operations
  It points to the top item of the stack
  It works with SS register (SS:SP)
BP (Base Pointer)
  The 16-bit BP register is the base pointer, mainly used to access parameters passed to the functions
  It also works with SS register (SS:BP)

## Slide 17: 3. Index Registers
Two 16-bit index registers are used for indexed addressing and sometimes used in addition and subtraction
SI - Source Index
DI - Destination Index

## Slide 18
Source Index (SI)
  It is used to store offset address of source operand
  It works with DS (DS:SI)
Destination Index (DI)
  It is used to store offset address of destination operand
  It works with ES (ES:DI)
Both SI and DI registers are used in string movement operations
Example
An instruction like movsb will copy a byte from the memory location pointed at/by SI, and move it to the memory location pointed at/by DI, and then increment both, so if you want to copy the byte stored at SI+1 to DI+1, it only takes a further movsb instruction

## Slide 19: Control Registers

## Slide 20: Control Registers
The 16-bit Instruction Pointer (IP) Register and Flags Register combined are considered as the control registers
Instruction Pointer (IP) Register
  It is used to store offset address of the next instruction to be executed
  It works with CS (CS:IP)

## Slide 21
Flags Register
  It is used to store the status value after arithmetic and logic operations that are tested by conditional instructions to change the flow of program execution
Common flag bits are:
  Sign Flag - SF
  Overflow Flag - OF
  Direction Flag - DF
  Interrupt Flag - IF
  Trap Flag - TF
  Zero Flag - ZF
  Auxiliary Flag - AF
  Parity Flag - PF
  Carry Flag - CF

## Slide 22
Video lecture can be accessed at
https://www.youtube.com/watch?v=tLzb6Sh0UiU