## Slide 1
Computer Organization & Assembly Language
Lecture 06
by Omar Bin Samin

## Slide 2: Today’s Discussion
Logical to Physical Address Conversion
Endianness

## Slide 3: Logical to Physical Address Conversion
Logical Address or Virtual Address
  An address generated by the CPU
Physical Address
  An address available on memory unit
Consider 12F3:4B27 (Logical Address)
Base/ Segment
Address
Offset Address

## Slide 4: General Knowledge
Base Address
  Starting Address of the segment
Offset Address
  Distance from the Base Address

## Slide 5
Put ‘o’ at the end of Base/ Segment Address and add it with Offset Address
1 2 F 3 o
0 4 B 2 7
1 7 A 5 7
12F3:4B27 corresponds to the physical address 0x17A57
+
1

## Slide 6: Task
Calculate the physical addresses for the given logical addresses:
  020A:1BCD
  001A:0021
  0FE1:2F22

## Slide 7: Endianness
Computers store data in memory in binary
The order in which bytes are stored is referred to as endianness. Endianness is of two types:
Little Endian
  When the least significant bytes are stored prior to most significant bytes
Big Endian
  When the most significant bytes are stored prior to least significant bytes

## Slide 8: Example
For “mov ax, 2” the machine code is “B80200”
“B8” is the machine code for “mov ax”
Data stored in ax is “0002”
MSB
LSB

## Slide 9
The data in memory can be stored as:
  0200 (LSB first and then MSB), Little Endian
  0002 (MSB first and then LSB), Big Endian
Intel architecture stores LSB to the lower address and MSB to higher address, hence following “Little Endian”

## Slide 10
Video lecture can be accessed at
https://www.youtube.com/watch?v=Lff8x-P7NJU