## Slide 1
Computer Organization & Assembly Language
Lecture 08
by Omar Bin Samin

## Slide 2: Today’s Discussion
What is db issue?
Addressing techniques

## Slide 3: db Issue
As discussed in previous lecture, using db with registers of 16-bits produces ambiguity in the results. Program discussed in previous lecture is as follows:
  [org 0x0100]
  mov ax,[Tag1]
  mov bx,4
  add ax,bx
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: db 2, 1

## Slide 4
The issue arises due to use of two consecutive bytes of separate data .i.e., first byte for ‘2’ (the data becomes ‘02’) and second byte for ‘1’ (the data becomes ‘01’) set by the following the command:
  Tag1: db 2, 1
While the command,
  mov ax,[Tag1]
moves the 16-bit (2 bytes) data from Tag1 to ‘ax’ in the form 0102, as the architecture is following little endian
The use of ‘ax’ register forced to move 2 bytes from the memory

## Slide 5
This issue can be resolved by replacing ‘ax’ with ‘al’ and ‘bx’ with ‘bl’, as ‘al’ and ‘bl’ refer to one byte each.
The program is given as follows:
  [org 0x0100]
  mov al,[Tag1]
  mov bl,4
  add al,bl
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: db 2, 1

## Slide 6: Listing File
  1 [org 0x0100]
  2 00000000 A0[0C00] mov al,[Tag1]
  3 00000003 B304 mov bl,4
  4 00000005 00D8 add al,bl
  5
  6 00000007 B8004C mov ax,0x4c00 ; exit
  7 0000000A CD21 int 0x21
  8
  9 0000000C 0201 Tag1: db 2, 1

## Slide 7: Task 01
Show the values (data) of ax, bx and Tag1 for all executable instructions:
  [org 0x0100]
  mov ah,[Tag1]
  mov bh,4
  add ah,bh
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: db 2, 1

## Slide 8: Task 02
Show the values (data) of ax, bx and Tag1 for all executable instructions:
  [org 0x0100]
  mov al,[Tag1]
  mov bh,4
  add al,bh
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: db 2, 1

## Slide 9: Tip
While programming in assembly language, people assume that the registers they are going to use are empty
This assuption may lead to undesirable results
To be on the safe side, either use “mov ax, 0” or “xor ax, ax” to clear the required register
Typically “xor ax, ax” is used to clear the register

## Slide 10: Addressing Techniques
The address field(s) in a typical instruction format is/ are relatively small
We would like to be able to reference a large range of locations in main memory
To achieve this objective, a variety of addressing techniques can be employed

## Slide 11
Most commonly used addressing techniques are:
  Immediate Addressing: the instruction itself contains the data to be loaded into the destination
  mov ax, 2
  Direct Addressing: the address field specifies which memory or register contains the operand/ data
  mov ax, [Tag1]

## Slide 12
  Indirect Addressing: the address field specifies which memory or register contains the address of an operand/ data
  mov dx, num1
  mov ax, [dx]
  Indexed Addressing: the address field consists of 2 parts:
    Index Memory/ Register Contents
    Constant
  The address field is the sum of index contents and a constant. It specifies which memory or register contains the operand
  mov ax, [Tag1+bx]

## Slide 13: Immediate Addressing
Consider the following piece of code:
  [org 0x0100]
  xor ax,ax
  xor bx,bx
  mov ax,2
  mov bx,4
  add ax,bx
  mov ax,0x4c00 ; exit
  int 0x21
Immediate Addressing

## Slide 14: Direct Addressing
Consider the following piece of code:
  [org 0x0100]
  xor ax,ax
  xor bx,bx
  mov ax,[Tag1]
  mov bx,4
  add ax,bx
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: dw 2, 1 ;Tag1 address = 111
Direct Addressing

## Slide 15: Indirect Addressing
Consider the following piece of code:
  [org 0x0100]
  xor ax,ax
  xor bx,bx
  mov bx,Tag1
  mov ax,[bx]
  mov dx,4
  add ax,dx
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: dw 2, 1 ;Tag1 address = 113
Indirect Addressing

## Slide 16: Indexed Addressing
Consider the following piece of code:
  [org 0x0100]
  xor ax,ax
  xor bx,bx
  mov bx,0
  mov ax,[Tag1+bx]
  mov dx,4
  add ax,dx
  mov ax,0x4c00 ; exit
  int 0x21
  Tag1: dw 2, 1 ;Tag1 address = 115
Indexed Addressing

## Slide 17
Video lecture can be accessed at
https://www.youtube.com/watch?v=SSpVAEcS-bs