## Slide 1
Computer Organization & Assembly Language
Lecture 09
by Omar Bin Samin

## Slide 2: Today’s Discussion
Flags

## Slide 3: Flags
Many instructions involve arithmetic and logical operations that changes the status of the flags, after which conditional instructions test the value of these status flags to take the control to the desired location
Common flag bits are:
  Overflow Flag - OF
  Direction Flag - DF
  Interrupt Flag - IF
  Sign Flag - SF
  Zero Flag - ZF
  Auxiliary Flag - AF
  Parity Flag - PF
  Carry Flag - CF
  Trap Flag - TF

## Slide 4: Overflow Flag (OF)
It indicates the overflow of a leftmost bit of data after a signed arithmetic operation
This flag is set to ‘1’, when there is a signed overflow
  Example
  (1000 0000)2+ (1000 0000)2 = (0000 0000) 2
This flag is set to ‘0’, there is no overflow
  Example
  (1111 0011)2+(0000 0001)2 = (1111 0100) 2

## Slide 5: OF: Examples
(1000 0000)2
(1000 0001)2
(0000 0001)2
OF = 1
+
(1000 0000)2
(0000 0001)2
(1000 0001)2
OF = 0
+
1

## Slide 6: OF: Example
(0001 0100 0000 1000)2
(1000 0100 0000 0000)2
(1001 0000 0000 1000)2
OF = 1
-
2

## Slide 7: Direction Flag
This flag is specifically used in string instructions
If directional flag is set (1), then access the string data from higher memory location towards lower memory location (Reverse Direction)
  Syntax: STD
If directional flag is reset (0), then access the string data from lower memory location towards higher memory location (Forward Direction)
  Syntax: CLD

## Slide 8: Interrupt Flag
It determines whether the external interrupts like keyboard entry, etc., are to be ignored or processed
It disables the external interrupt when the value is reset (0) and enables interrupt when set (1)

## Slide 9: Sign Flag (SF)
It shows the sign of the result of an arithmetic or logical operation
The sign is indicated by the leftmost bit
A positive result clears the value of SF to ‘0’ and negative result sets it to ‘1’

## Slide 10: SF: Examples
(1000 0000)2
(0000 0001)2
(1000 0001)2
SF = 1
+
(0000 0000)2
(0000 0001)2
(0000 0001)2
SF = 0
+

## Slide 11: SF: Example
(0001 0100 0000 1000)2
(1000 0100 0000 0000)2
(1001 0000 0000 1000)2
SF = 1
-
2

## Slide 12: Zero Flag (ZF)
Indicates zero result
This flag is set to ‘1’, when result is zero
  Example: 2-2 = 0
This flag is set to ‘0’, when result is non- zero
  Example: 3-2 = 1

## Slide 13: ZF: Examples
(1000 0000)2
(1000 0000)2
(0000 0000)2
ZF = 1
+
(0000 0000)2
(0000 0001)2
(0000 0001)2
ZF = 0
+

## Slide 14: ZF: Example
(1000 0100 0000 1000)2
(1000 0100 0000 1000)2
(0000 0000 0000 0000)2
ZF = 1
-

## Slide 15: Auxiliary Flag (AF)
Indicates whether an operation produced a carry or borrow in the low-order 4 bits (nibble)
For 16-bit values, only the least significant 8-bits are considered for computing auxiliary flag value

## Slide 16: AF: Examples
(0000 1000)2
(0000 1001)2
(0001 0001)2
AF = 1
+
(0000 0000)2
(0000 0001)2
(0000 0001)2
AF = 0
+
1

## Slide 17: AF: Example
(0000 1000 0000 1000)2
(1000 1000 0000 0000)2
(1001 0000 0000 1000)2
AF = 0
+
1

## Slide 18: Parity Flag (PF)
Indicates even parity of the low 8-bits of the result
PF is set to ‘1’, if the lower 8-bits contain even number of 1
For 16-bit values, only the least significant 8-bits are considered for computing parity value

## Slide 19: PF: Examples
(0000 1000)2
(0000 1001)2
(0001 0001)2
PF = 1
+
(0000 0000)2
(0000 0001)2
(0000 0001)2
PF = 0
+
1

## Slide 20: PF: Example
(0000 1000 0001 1000)2
(0000 1000 0000 0000)2
(0001 0000 0001 1000)2
PF = 1
+
1

## Slide 21: Carry Flag (CF)
Records the fact that the result of an arithmetic operation on unsigned numbers is in range or out of range
This flag is set to ‘1’, when result is out of range
  Example
  (1111 1111)2+(0000 0001)2 = (1 0000 0000) 2
This flag is set to ‘0’, when result is in range
  Example
  (1111 0011)2+(0000 0001)2 = (1111 0100) 2

## Slide 22: CF: Examples
(1100 1000)2
(1100 1001)2
(1001 0001)2
CF = 1
+
(0000 0000)2
(0000 0001)2
(0000 0001)2
CF = 0
+
1
1

## Slide 23: CF: Example
(0000 1000 0001 1000)2
(1000 1000 0000 0000)2
(1000 0000 0001 1000)2
CF = 1
-
2

## Slide 24: Trap Flag (TF)
It allows setting the operation of the processor in single step mode
Example
  The DEBUG program we used, sets the trap flag to ‘1’, so we could step through executing one instruction at a time

## Slide 25: Example
Consider the following piece of code and show the values of ax, bx, OF, IF, SF, ZF, AF, PF and CF.
  [org 0x0100]
  mov al,10
  mov bl,1
  sub ah, bl
  add al,ah
  Mov ax,oxffff
  xor ax,ax
  mov ax,0x4c00 ; exit
  int 0x21

## Slide 26
Instructions | AX | BX | OF | IF | SF | ZF | AF | PF | CF
[org 0x0100] |  |  |  |  |  |  |  |  | 
mov al,10 | 00 0A | 00 00 | 0 | 1 | 0 | 0 | 0 | 0 | 0
mov bl,1 | 00 0A | 00 01 | 0 | 1 | 0 | 0 | 0 | 0 | 0
sub ah, bl | FF 0A | 00 01 | 0 | 1 | 1 | 0 | 1 | 1 | 1
add al,ah | FF 09 | 00 01 | 0 | 1 | 0 | 0 | 1 | 1 | 1
Mov ax,oxffff | FF FF | 00 01 | 0 | 1 | 0 | 0 | 1 | 1 | 1
xor ax,ax | 00 00 | 00 01 | 0 | 1 | 0 | 1 | 0 | 1 | 0
mov ax,0x4c00 |  |  |  |  |  |  |  |  | 
int 0x21 |  |  |  |  |  |  |  |  | 

## Slide 27: Task
Consider the following piece of code and show the values of ax, bx, OF, IF, SF, ZF, AF, PF and CF.
  [org 0x0100]
  xor ax,ax
  mov al,12
  mov bl,5
  sub ah, bl
  add ah,ah
  mov ah,al
  add al,bl
  mov ax,oxffff
  xor ax,ax
  mov ax,0x4c00 ; exit
  int 0x21

## Slide 28
Video lecture can be accessed at
https://www.youtube.com/watch?v=kBra1qUlUwU